gp165-2 Training flanged basketball board  90 × 120 cm

- satisfies all of  FIBA requirements, except for an external size

- openings for rings with the standard base, particularly fit to gp165-0 and gp165

- flanging provides high ruggedness of a board, absolute stability to the repeated impacts

#### Manual

Assembling and installation

In order to attach the product to a wall:

- Take off the bibbs

- Place the assembled product against the wall and mark spots for the anchor bolts (not in a set).

- Bore holes on the marked spots with a drill of 10 mm in diameter for anchor bolt 10 x 80 at least 80 mm deep.

- Insert the anchor bolts (do not untwist them) into the holes  through the fixing elements of the product. Hammer them the full length. Tighten the anchor bolt heads with a spanner.

Insert the bibbs back.

Bolting is admitted. Bolt body is 10 mm in diameter.

warranty

Warranty period: 3 years from the day of sale. Operation period: unlimited.

# Text boxes

Works number__________________________

Packer________________________________

Date of packing ________________________

Quality engineer   ______________________

Address:

Sporting goods factory LECO,

Russia, 141830, Moscow region, Dmitrov district, Synkovo town

Web-address:

www.leco.msk.ru