gp257-1 Basic home metal sportcomplex,

height 2,35 - 3,20m

Manual

Purpose: basic sport set for sport exercises for amateur and professional sportsmen, together with the additional children equipment may be used for kids games.

Design features:

- safety (possibility of loss of stability is structurally excluded);

- simplicity and ease of installation (installation is made by one person with little effort);

- two types of installation:

- 1.Symmetric - for big loads

- 2.Asymmetrical - allows to install a complex close to a wall;

- adjusting details are hidden in the construction giving stylish slick look

- compact gift package

Sports equipment:

- Wall Bars,

- Parallel Bars,

- Horizontal Bar with Wide Grip.

Construction features

- width of the Wall Bars, cm                                                  – 60

- width of horizontal bars, сm                                                – 93

- diameter of main bar of wall bars, mm                                – 26

- maximal load, symmetrical installation, kg                         – unlimited if used properly

- maximal load, asymmetrical installation, kg                        – 100

- weight, kg                                                                             – 18

the components SET

| Item number | Name | Quantity |
| --- | --- | --- |
| 1 | Beam | 2 |
| 2 | Lower prop | 2 |
| 3 | Middle prop | 2 |
| 4 | Short spacer | 2 |
| 5 | Long spacer | 2 |
| 6 | Prop raise | 2 |
| 7 | Long crossbar | 10 |
| 8 | Short crossbar | 2 |
| 9 | Horizontal bar prop | 2 |
| 10 | Horizontal cross-beam | 1 |
| 11 | Skids girder | 2 |
| 12 | Diagonal brace | 2 |
| 13 | Bars straight arch | 2 |
| 14 | Upper stop | 4 |
| 15 | Horizontal bar support | 2 |
| 16 | Upper skids support | 2 |
| 17 | Large bearing heel of the regulation screw | 2 |
| 18 | Tap-wrench | 1 |
| 19 | Bushing of 37.5 mm in diameter | 2 |
| 20 | Bushing of attachable equipment | 3 |
| 21 | Decorative case 35 mm | 2 |
| 22 | Bolt М10х60 | 4 |
| 23 | Screw 6х40 | 2 |
| 24 | Screw 6х45 | 4 |
| 25 | Screw 6х50 | 30 |
| 26 | Screw 6х50 countersunk | 2 |
| 27 | Nut М6 | 4 |
| 28 | Wacher 6 enlarged | 2 |
| 29 | Washer 10 enlarged | 2 |

Attention! In some of LECO goods small ironware and wiffets are packed up within the large parts.

assembling and Installation

ATTENTION! The figures given below are taken from the technical assembling drawings of the specified product. The numbers and colors of the components correspond to those in section “LIST OF COMPONENTS”. Before starting assembling, perform the COMPLETE IDENTIFICATION OF THE COMPONENTS and separate them according to the table. For this, use the photographs of the product on the package together with the drawings and the table with the specified names and quantities of the components. Identification of the components before assembling helps significantly to comprehend the figures and shortens assembling time.

A particular feature of assembling is in the need to mount firstly the thrust prop ready-mounted with the beam. Next, tighten the crossbars to the fixed prop with the beam. The second prop with the beam must be tightened then. After that straighten upright  both of the props and thrust the sport set with the screws. Adjust the spacers #4 and #5 if it is necessary depending on ceiling height.

Fig.1. General view (symmetrical installation, maximal height)

warranty

Warranty period: 3 years from the day of sale. Operation period: unlimited.

# Text boxes

Address:

Sporting goods factory LECO,

Russia, 141830, Moscow region, Dmitrov district, Synkovo town

Web-address:

www.leco.msk.ru

Works number__________________________

Packer________________________________

Date of packing ________________________

Quality engineer   ______________________