gp257-2 Home metal sport set with horizontal bar and  attached equipment height 2,35 - 3,20m

Manual

Purpose: for games and sport exercises for children and adults

Design features:

- safety (possibility of loss of stability is structurally excluded);

- simplicity and ease of installation (installation is made by one person with little effort);

- two types of installation:

1.Symmetric - for big loads

2.Asymmetrical - allows to install a complex close to a wall;

- adjusting details are hidden in the construction giving stylish slick look

Sports equipment:

- Wall Bars,

- Horizontal Bar with Wide Grip

- gymnastic rings, diameter 15 cm

- rope ladder

- swing disc

- trapeze.

Construction features

- width of the Wall Bars, cm                                                  – 45

- width of horizontal bars, сm                                                – 80

- diameter of main bar of wall bars, mm                                – 22

- maximal load, symmetrical installation, kg                         – unlimited if used properly

- maximal load, asymmetrical installation, kg                        – 100

the components SET

| Item number | Name | Quantity |
| --- | --- | --- |
| 1 | Beam | 2 |
| 2 | Lower prop | 2 |
| 3 | Middle prop | 2 |
| 4 | Short spacer | 2 |
| 5 | Long spacer | 2 |
| 6 | Prop raise | 2 |
| 7 | Long crossbar | 10 |
| 8 | Short crossbar | 2 |
| 9 | Horizontal bar prop | 2 |
| 10 | Horizontal cross-beam | 1 |
| 11 | Upper support | 4 |
| 12 | Short cord with slip block | 2 |
| 13 | Long cord with slip block | 2 |
| 14 | Cord for swing disc | 1 |
| 15 | Cord for rope ladder | 2 |
| 16 | Gymnastic ring | 2 |
| 17 | Swing disc | 1 |
| 18 | Wooden crossbar for the Trapeze | 1 |
| 19 | Wooden crossbar for the Rope Ladder | 8 |
| 20 | Horizontal bar support | 2 |
| 21 | Large bearing heel of the regulation screw | 2 |
| 22 | Tap-wrench | 1 |
| 23 | Bushing of 37.5 mm in diameter | 2 |
| 24 | Plastic bushing 6 mm for cord, L=50мм | 3 |
| 25 | Decorative case | 2 |
| 26 | Bolt M10x60 | 4 |
| 27 | Screw 6x50 | 30 |
| 28 | Nut 10 enlarged | 2 |

Attention! In some of LECO goods small ironware and wiffets are packed up within the large parts.

assembling and Installation

ATTENTION! The figures given below are taken from the technical assembling drawings of the specified product. The numbers and colors of the components correspond to those in section “LIST OF COMPONENTS”. Before starting assembling, perform the COMPLETE IDENTIFICATION OF THE COMPONENTS and separate them according to the table. For this, use the photographs of the product on the package together with the drawings and the table with the specified names and quantities of the components. Identification of the components before assembling helps significantly to comprehend the figures and shortens assembling time.

A particular feature of assembling is in the need to mount firstly the thrust prop ready-mounted with the beam. Next, tighten the crossbars to the fixed prop with the beam. The second prop with the beam must be tightened then. After that straighten upright  both of the props and thrust the sport set with the screws. Adjust the spacers #4 and #5 if it is necessary depending on ceiling height.

While you are busy with assembling the Home Sport Set for Kids, your child may start assembling the rope ladder with your help and under your supervision (excellent developing exercise). Depending on the child’s height, the steps of the ladder can be assembled at different distance from one another. As follows from experience, it is most comfortable for children to climb a rope ladder with a distance between the steps of not more than the shank’s length. The knots should be tightened the same way as two existing knots (so-called “simple knots”) at the rope ends. The ladder assembling is performed from the top down. Place the cords with the knots upward. Thread the cords into the first bar, see Fig.1. The grooves for the knots on the bar must be at the bottom. Tie the knots without tightening to make them movable. Thread the cords into the second bar and bind the knots for it at a chosen distance from the first bar, and so on. The ladder can be rebound for a fully-grown child.

Pic.1. Rope ladder assembling

Pic.2. General view (symmetrical installation, maximal height).

Assembling and setting-up attached equipment

It is recommended to hang up the attached equipment after the Sport Set is completely set up. One of the possibilities of setting it up is shown in Fig.2. One may choose one’s own way. Choose places on the beams for setting up the rope ladder and gymnastic rings. Insert the plastic hubs into the inlets on the beams. Thread the cord ends into the hubs. Tie “simple knots” on the top ends of the cords, see Table 1. Fix the gymnastic rings with the “figure-eight” knot or “slip-knot”. This system of cord fixation ensures full absence of abrasive wearing and provides reliability of suspension.

Table 1

| Name of the not | Appearance of the knot and ways of tying | Recommendations for its use |
| --- | --- | --- |
| Slip-knot |  | Nice knot with the function of the running knot. Used for fixing slip blocks and gymnastic rings. |
| Figure-eight |  | Main fixing knot for suspension. Used for fastening slip blocks and gymnastic rings. |
| Simple |  | Knot for local widening of the rope in order to limit it’s movement. Used for fastening the rope ladder bars and trapeze one. |

warranty

Warranty period: 3 years from the day of sale.

# Text boxes

Works number__________________________

Packer________________________________

Date of packing ________________________

Quality engineer   ______________________

Address:

Sporting goods factory LECO,

Russia, 141830, Moscow region, Dmitrov district, Synkovo town

Web-address:

www.leco.msk.ru