gp258 Wall sportcomplex for kids

Purpose: for games and sport exercises for children 3-14 years of age

Design features: Wall Bars, Gymnastics Rings of 15cm in diameter, Rope Ladder, Trapeze.

Manual

TECHNICAL CHARACTERISTICS

-  height, сm		                        - 225,

-  maximal load, kg			- 100,

-  diameter of the bar, mm		- 22,

-  wall bars width, cm                          - 50.

THE LIST OF componentS

| Item number | Name | Quantity |
| --- | --- | --- |
| 1 | Prop | 2 |
| 2 | Crossbar | 10 |
| 3 | Left beam | 1 |
| 4 | Right beam | 1 |
| 5 | Bracket | 4 |
| 6 | Short cord | 2 |
| 7 | Gymnastics ring | 2 |
| 8 | Long cord with slip blocks | 2 |
| 9 | Trapeze bar | 1 |
| 10 | Cord for the rope ladder | 2 |
| 11 | Bar for the rope ladder | 8 |
| 12 | Plastic hub for the cord | 4 |
| 13 | Screw М6х35 | 20 |
| 14 | Dowel 8х50 | 4 |
| 15 | Self-cutting screw 4,2х50 | 4 |
| 16 | Anchor bolt 8х80 | 2 |
| 17 | Pipe bearing 40x20 | 2 |

Attention! In some of LECO goods small ironware and wiffets are packed up within the large parts.

assembling and Installation

ATTENTION! The figures given below are taken from the technical assembling drawings of the specified product. The numbers and colors of the components correspond to those in section “LIST OF COMPONENTS”. Before starting assembling, perform the COMPLETE IDENTIFICATION OF THE COMPONENTS and separate them according to the table. For this, use the photographs of the product on the package together with the drawings and the table with the specified names and quantities of the components. Identification of the components before assembling helps significantly to comprehend the figures and shortens assembling time.

Rope Ladder Assembling

While you are busy with assembling the Wall Sport Complex for Kids, your child may start assembling the rope ladder with your help and under your supervision (excellent developing exercise). Depending on the child’s height, the steps of the ladder can be assembled at different distance from one another. As follows from experience, it is most comfortable for children to climb a rope with a distance between the steps of not more than the shank’s length. The knots should be tightened the same way as two existing knots (so-called “simple knots”) at the rope ends. The ladder assembling is performed from the top down. Place the cords with the knots upward. Thread the cords into the first bar, see Fig.1. The grooves for the knots on the bar must be at the bottom. Tie the knots without tightening to make them movable. Thread the cords into the second bar and bind the knots for it at a chosen distance from the first bar, and so on. The ladder can be rebound for a fully-grown child.

Fig.1

Two types of anchor bolts are used at the Sporting Goods Factory “LECO”: 8x80 and 10x80.

In order to attach the product to a wall:

1. Place the assembled product against the wall and mark spots for the anchor bolts.

2. Bore holes on the marked spots with a drill of 8 mm in diameter (a drill of 10 mm in diameter for the 10x80 bolt) at least 80 mm deep.

3. Before fastening the sport set to the wall dismantle the anchor bolts previously and insert it in fastening apertures of the beams item 3 and 4 (the nuts must be under bolt’s heads). Assemble the anchor bolts, which are situated in beams fastening apertures.

4. Insert the anchor bolts the full length in the top holes . Tighten the anchor bolt heads.

Pic.2

Assembling and setting-up attached equipment

It is recommended to hang up the attached equipment after the Sport Complex is completely set up. One of the possibilities of setting it up is shown in Fig.1. One may choose one’s own way. Choose places on the beams for setting up the rope ladder and gymnastic rings. Insert the plastic hubs into the inlets on the beams. Thread the cord ends into the hubs. Tie “simple knots” on the top ends of the cords, see Table 1. Fix the gymnastic rings with the “figure-eight” knot or “slip-knot”. This system of cord fixation ensures full absence of abrasive wearing and provides reliability of suspension.

Table 1.

| Name of the not | Appearance of the knot and ways of tying | Recommendations for its use |
| --- | --- | --- |
| Slip-knot |  | Nice knot with the function of the running knot. Used for fixing slip blocks and gymnastic rings. |
| Figure-eight |  | Main fixing knot for suspension. Used for fastening slip blocks and gymnastic rings. |
| Simple |  | Knot for local widening of the rope in order to limit its movement. Used for fastening the rope ladder bars and trapeze one. |

warranty

Warranty period: 2 years from the day of sale.

# Text boxes

Works number__________________________

Packer________________________________

Date of packing ________________________

Quality engineer   ______________________

Address:

Sporting goods factory LECO,

Russia, 141830, Moscow region, Dmitrov district, Synkovo town

Web-address:

www.leco.msk.ru