GP259 WALL BASIC HOME SPORTCOMPLEX

Basic sport complex for sport exercises for amateurs and professional sportsmen, together with the additional children equipment may be used for kids games.

Includes Wall bars, Parallel Bars, Horizontal Bar with Wide Grip.

Manual

Construction features.

- width of Wall bars, cm                                                                                 - 60;

- width of Horizontal Bar, cm                                                                         - 93;

- diameter of a bar, mm                                                                                  - 25;

- maximal load is unlimited if used properly

- weight, kg                                                                                                      - 4

THE LIST OF componentS

| Item number | Name | quantity |
| --- | --- | --- |
| 1 | Prop | 2 |
| 2 | Crossbar | 9 |
| 3 | Left beam | 1 |
| 4 | Right beam | 1 |
| 5 | Bracket | 4 |
| 6 | Horizontal bar | 1 |
| 7 | Horizontal bar support | 2 |
| 8 | Parallel bars handle | 2 |
| 9 | Upper support | 2 |
| 10 | Lower support | 2 |
| 11 | Parallel bars brace | 2 |
| 12 | Bars straight arch | 2 |
| 13 | Plastic hub for the cord | 4 |
| 14 | Bolt М8х45 | 2 |
| 15 | Screw М6х40 | 20 |
| 16 | Screw М6х45 | 4 |
| 17 | Screw М6х50 countersunk | 2 |
| 18 | Screw-nut М6 | 4 |
| 19 | Screw-nut М8 | 2 |
| 20 | Washer М6 enlarged | 2 |
| 21 | Dowel 8х50 | 4 |
| 22 | Screw 4,2х50 | 4 |
| 23 | Anchor bolt 10х80 | 2 |

Attention! In some of LECO goods small ironware and wiffets are packed up within the large parts.

assembling and Installation

ATTENTION! The figures given below are taken from the technical assembling drawings of the specified product. The numbers and colors of the components correspond to those in section “LIST OF COMPONENTS”. Before starting assembling, perform the COMPLETE IDENTIFICATION OF THE COMPONENTS and separate them according to the table. For this, use the photographs of the product on the package together with the drawings and the table with the specified names and quantities of the components. Identification of the components before assembling helps significantly to comprehend the figures and shortens assembling time.

Two types of anchor bolts are used at the Sporting Goods Factory “LECO”: 8x80 and 10x80.

In order to attach the product to a wall:

1. Place the assembled product against the wall and mark spots for the anchor bolts.

2. Bore holes on the marked spots with a drill of 8 mm in diameter (a drill of 10 mm in diameter for the 10x80 bolt) at least 80 mm deep.

3. Before fastening the sport set to the wall dismantle the anchor bolts previously and insert it in fastening apertures of the beams item 3 and 4 (the nuts must be under bolt’s heads). Assemble the anchor bolts, which are situated in beams fastening apertures.

4. Insert the anchor bolts the full length in the top holes . Tighten the anchor bolt heads.

warranty

Warranty period: 3 years from the day of sale.

Operation period: unlimited.

# Text boxes

Works number__________________________

Packer________________________________

Date of packing ________________________

Quality engineer   ______________________

Address:

Sporting goods factory LECO,

Russia, 141830, Moscow region, Dmitrov district, Synkovo town

Web-address:

www.leco.msk.ru