#### gp289 Wall horizontal bar 80 cm

- 40 cm wall gap,

- it is possible to attach children gymnastics rings

- attached to the wall with two anchors and two screws

#### Manual

TECHNICAL CHARACTERISTICS

- diameter of a bar, mm              – 28 (standard for gymnastics cross-beams)

- maximal load                            – unlimited if used properly

THE LIST OF componentS

| Item number | Name | Quantity |
| --- | --- | --- |
| 1 | Bracket | 2 |
| 2 | Bar | 1 |
| 3 | Anchor bolt 8х80 | 2 |
| 4 | Self-cutting screw 5х35 | 2 |
| 5 | Dowel 8х30 | 2 |
| 6 | Screw 6х10 | 2 |
| 7 | Nut M6 | 2 |

Attention! In some of LECO goods small ironware and wiffets are packed up within the large parts.

assembling and Installation

ATTENTION! The figures given below are taken from the technical assembling drawings of the specified product. The numbers and colors of the components correspond to those in section “LIST OF COMPONENTS”. Before starting assembling, perform the COMPLETE IDENTIFICATION OF THE COMPONENTS and separate them according to the table. For this, use the photographs of the product on the package together with the drawings and the table with the specified names and quantities of the components. Identification of the components before assembling helps significantly to comprehend the figures and shortens assembling time.

Two types of anchor bolts are used at the Sporting Goods Factory “LECO” --  8x80 and 10x80.

In order to attach the product to a wall:

1. Place the assembled product against the wall and mark spots for the anchor bolts.

2. Bore holes on the marked spots with a drill of 8 mm in diameter (a drill of 10 mm in diameter for the 8x80 bolt) at least 80 mm deep.

3. Insert the anchor bolts (do not untwist them) into the top holes through the fixing elements of the product. Hammer in the anchor bolts the full length. Tighten the anchor bolt heads with a spanner.

warranty

Warranty period: 3 years from the day of sale.

# Text boxes

Address:

Sporting goods factory LECO,

Russia, 141830, Moscow region, Dmitrov district, Synkovo town

Web-address:

www.leco.msk.ru

Works number__________________________

Packer________________________________

Date of packing ________________________

Quality engineer   ______________________