#### gp357  wall boxing bag

- filling -- foamed PE and foamed PU,

- “hands friendly” during training,

- the ability of 2 variants of installation -- bag up and bag down, in down case there is ability to train low kicks,

- the bag is installed on the absorber with 3 springs providing "correct" behaviour of a bag during training,

- it is intended for trainings for amateurs and professional sportsmen,

- the bracket of a bag fastens to wall by 4 anchors

#### Manual

TECHNICAL CHARACTERISTICS

- diameter of a bag, cm              – 34

- height of a bag, cm                  – 100

- weight, kg                                – 14

THE LIST OF componentS

| Item number | Name | Quantity |
| --- | --- | --- |
| 1 | Boxing bag with fastening system | 1 |
| 2 | Bracket | 1 |
| 3 | Anchor bolt 10х80 | 4 |
| 4 | Bolt 8х20 | 2 |
| 5 | Self-locking nut М8 | 1 |

Attention! In some of LECO goods small ironware and wiffets are packed up within the large parts

assembling and Installation

ATTENTION! The figures given below are taken from the technical assembling drawings of the specified product. The numbers and colors of the components correspond to those in section “LIST OF COMPONENTS”.

Two types of anchor bolts are used at the Sporting Goods Factory “LECO”: 8x80 and 10x80.

In order to attach the product to a wall:

1. Place the assembled product against the wall and mark spots for the anchor bolts.

2. Bore holes on the marked spots with a drill of 8 mm in diameter (a drill of 10 mm in diameter for the 10x80 bolt) at least 80 mm deep.

3. Insert the anchor bolts (do not untwist them) into the top holes through the fixing elements of the product. Hammer in the anchor bolts the full length. Tighten the anchor bolt heads with a spanner.

warranty

Warranty period: 5 years from the day of sale. Operation period: unlimited.

# Text boxes

Address:

Sporting goods factory LECO,

Russia, 141830, Moscow region, Dmitrov district, Synkovo town

Web-address:

www.leco.msk.ru

Works number__________________________

Packer________________________________

Date of packing ________________________

Quality engineer   ______________________