#### gp400  wall mounted horizontal bar 100 cm

#### with hanging equipment attaching system

- Construction reinforcement,

- wall space – 60 cm,

- additionally supplied with a ring-bolt to hang heavy boxing bags and plugs to attach children sport equipment (rope ladder, rope, rings),

- fastening to the wall with four anchors

#### Manual

TECHNICAL CHARACTERISTICS

- diameter of a bar, mm              – 28 (standard for gymnastics cross-beams)

- weight, kg                                 –  3

- maximal load                            – unlimited if used properly

THE LIST OF componentS

| Item number | Name | Quantity |
| --- | --- | --- |
| 1 | Bracket | 2 |
| 2 | Bar | 1 |
| 3 | Ring-nut | 1 |
| 4 | Plastic bushuing | 3 |
| 5 | Bolt M 8х40 | 2 |
| 6 | Anchor bolt 10х80 | 4 |
| 7 | Nut M8 | 2 |
| 8 | Bolt 8x45 | 1 |
| 9 | Nut 8 enlarged | 1 |
| 10 | Spring washer | 1 |

Attention! In some of LECO goods small ironware and wiffets are packed up within the large parts.

assembling and Installation

ATTENTION! The figures given below are taken from the technical assembling drawings of the specified product. The numbers and colors of the components correspond to those in section “LIST OF COMPONENTS”. Before starting assembling, perform the COMPLETE IDENTIFICATION OF THE COMPONENTS and separate them according to the table. For this, use the photographs of the product on the package together with the drawings and the table with the specified names and quantities of the components. Identification of the components before assembling helps significantly to comprehend the figures and shortens assembling time.

Two types of anchor bolts are used at the Sporting Goods Factory “LECO”: 8x80 and 10x80.

In order to attach the product to a wall:

1. Place the assembled product against the wall and mark spots for the anchor bolts.

2. Bore holes on the marked spots with a drill of 8 mm in diameter (a drill of 10 mm in diameter for the 10x80 bolt) at least 80 mm deep.

3. Insert the anchor bolts (do not untwist them) into the top holes through the fixing elements of the product. Hammer in the anchor bolts the full length. Tighten the anchor bolt heads with a spanner.

warranty

Warranty period: 3 years from the day of sale.

# Text boxes

Works number__________________________

Packer________________________________

Date of packing ________________________

Quality engineer   ______________________

Address:

Sporting goods factory LECO,

Russia, 141830, Moscow region, Dmitrov district, Synkovo town

Web-address:

www.leco.msk.ru