GP403 Horizontal Bar + bars double side stand

#### adjustable height (two positions for horizontal bar),

#### horizontal bar with inclined handles for pull ups with normal and wide grip,

#### additionally provided with special system for hanging heavy boxing bag (in this case needs additional fastening to the floor through special openings),

#### provided with special plugs, which allow to hang special sport equipment for children (rope-ladder, rope, rings),

#### includes vertical and horizontal handles, also elbow and back rests, which allow to perform different exercises

#### Manual

TECHNICAL CHARACTERISTICS

- length, cm                                                                                              – 156

- width,                                                                                                    – 106

- height, cm                                                                                             – 231

- maximal load (weight of user and boxing bag), kg                              – 150

- weight of a training machine, kg                                                           – 28

The List of components

| Item number | Name | Quantity |
| --- | --- | --- |
| 1 | Lower beam | 2 |
| 2 | Prop | 2 |
| 3 | Diagonal brace with steps | 2 |
| 4 | Prop extension | 2 |
| 5 | Prop crosspiece | 1 |
| 6 | Push- up bar | 2 |
| 7 | Horizontal bar bracket | 2 |
| 8 | Horizontal bar crossbeam | 1 |
| 9 | Crossbeam handle | 2 |
| 10 | Parallel bars bracket | 2 |
| 11 | Parallel bars crosspiece | 1 |
| 12 | Back rest holder | 1 |
| 13 | Vertical handle | 2 |
| 14 | Back rest | 1 |
| 15 | Elbow-rest | 2 |
| 16 | Square bibb | 6 |
| 17 | Round bibb | 4 |
| 18 | Bushing for the attached equipment | 3 |
| 19 | Bolt М8х40 | 7 |
| 20 | Bolt М8х90 | 4 |
| 21 | Bolt М6х12 | 2 |
| 22 | Bolt М6х40 | 4 |
| 23 | Countersunk screw М6х35 | 2 |
| 24 | Screw М6х45 | 2 |
| 25 | Countersunk screw М8х60 | 20 |
| 26 | Nut M8 | 30 |
| 27 | Nut M6 | 2 |
| 28 | Ring-nut М8 | 1 |
| 29 | Washer 8 enlarged | 5 |
| 30 | Spring washer 8 | 1 |
| 31 | Washer 6 enlarged | 4 |
| 32 | Washer 12 | 20 |
| 33 | Self-cutting screw 6х50 | 4 |
| 34 | Dowel 10х50 | 4 |

Attention! In some of LECO goods small ironware and wiffets are packed up within the large parts.

assembling and Installation

ATTENTION! The figures given below are taken from the technical assembling drawings of the specified product. The numbers and colors of the components correspond to those in section “LIST OF COMPONENTS”. Before starting assembling, perform the COMPLETE IDENTIFICATION OF THE COMPONENTS and separate them according to the table. For this, use the photographs of the product on the package together with the drawings and the table with the specified names and quantities of the components. Identification of the components before assembling helps significantly to comprehend the figures and shortens assembling time.

A particular feature of the Stand assembling is in the need to connect all elements first on one side and then on the other one. Next, two sides must be linked together by means of two cross-pieces and the horizontal bar.

Tighten the M8 screw with a screwdriver while holding the nut with the 13 mm spanner, but not the other way around.

Do not tighten the fasteners immediately with a heavy strain. Finish tightening all screws after final positioning of the stand on a chosen spot and when all fasteners are set in.

Warranty period: 3 years from the day of sale.

Operation period: unlimited.

Fig.1. Right-side view.

Fig.2. Front View.

# Text boxes

Address:

Sporting goods factory LECO,

Russia, 141830, Moscow region, Dmitrov district, Synkovo town

Web-address:

www.leco.msk.ru

Works number__________________________

Packer________________________________

Date of packing ________________________

Quality engineer   ______________________